SAMPLE of FINAL EXAM

General requirements for the exam:

- This is CLOSED BOOK examination;

- No questions allowed within examination period;

- If  something is not clear in question please, put your assumptions;

- No extra papers cell-phones or programmable calculators are allowed;

- For calculations or assumptions you can use reserved space in the exam paper or opposite side of each page;

- It is allowed for use: Pens and pencils, erasers, simple calculators and rulers.

Design and Verification of Embedded System around Processing Core

The embedded system consists of the following major components: 1) Virtual memory subsystem including Cache, SDRAM and Hard Disk Drive, 2) Video-output subsystem and 3) I/O Subsystem on the base of Peripheral Processing Unit (I/O Processor).

Specification of each component is given in appropriate section. The design estimation and verification procedures have to be completed prior to design stage.

Section 1: Memory subsystem organization

The memory subsystem is organized as virtual memory including Page Table Register, TLB and two-way associative cache implemented in the FPGA. Cache controller incorporated in the FPGA provides interfacing between the Cache and Main memory implemented in SDRAM-module. Virtual memory controller allocated also in the FPGA provides page exchange process between Main memory and Hard Disk Drive (HDD) via I/O subsystem interface. The block diagram of the memory subsystem is shown in Fig. 1.

Figure 1: Block diagram of memory subsystem

Memory subsystem specifications:

- Virtual memory should provide direct addressing of 4G words. Data word = 4Bytes

- Main memory (SDRAM) should provide 4GB (1G x 32 bit) memory space

- SDRAM allows DDR (Double-Data Rate) access with clock frequency = 133.3 MHz

- CPU provides bus clock frequency = 266.6 MHz and pipelined Address / Data transmission (no address overhead).

Question 1.1:

Estimate organization of the bus between cache controller (in the FPGA) and CPU:

1) Bus type (circle the correct variant):                                                                  (1 mark)

a) Parallel synchronous;              b) Serial synchronous

c) Parallel asynchronous;            d) Serial asynchronous

2) Number of FPGA pins reserved for the CPU VM address lines = ________    (1 mark)

Show calculations:_______________________________________________________

3) Number of FPGA pins reserved for the CPU Data lines    = ________            (1 mark)

4) Circle control signals which must be used for CPU-to-Cache interface           (2 marks)

Control lines:    RAS;    CAS;     WE;    OE;    Clock;    Byte select

5) Calculate CPU Data Bus bandwidth = _____________ MB/sec                    (2 marks)

Show calculations: _______________________________________________________

Question 1.2:

Estimate bus organization between the cache (in the FPGA) & Main memory (SDRAM):

1) Bus type (circle the correct variant):                                                                 (1 mark)

a) Parallel synchronous;              b) Serial synchronous

c) Parallel asynchronous;            d) Serial asynchronous

2) Number of FPGA pins reserved for SDRAM address lines = ____________ (2 marks)

Show calculations:_______________________________________________________

3) Number of FPGA pins reserved for the Memory Data lines    = ________     (1 mark)

4) Circle strobe &synchronization signals used for cache-to-SDRAM interface (2 marks)

Strobe & synchronization lines:    RAS;    CAS;     WE;    OE;    Clock;    Busy.

5) Calculate SDRAM Data Bus bandwidth = _____________ MB/sec               (2 marks)

Show calculations:________________________________________________

Section 2: Virtual memory and Cache interaction

To check the interaction between components of virtual memory and the two-way set associative cache, the test program segment has been loaded to the memory subsystem. The contents of all elements of virtual memory and cache after the above process are presented below.

The contents of fully associative TLB and Page Table Register (PTR) are shown in Figure 2. The Figure 3 presents the content of the Page Table in the Main memory.

Page size = 16 KB (4K x 32 bits). Word size = 32 bits (4 Bytes).

Note: Page is word addressable

Two-way set associative cache is organized as: 2 sets of 8 entries x 2 word in block device (See Figure 4). The NRU (Not Recently Used) block replacement mechanism is implemented with one Reference bit (R). R becomes = 1 when the cache entry is recently used. Otherwise, R = 0 when another cache bank entry is selected (with the same index). If miss occurs the block which indicated R=0 will be replaced. If R-bits in both Cache entries in the Cache Bank 0 and Cache Bank 1 are = 0, the cache entry in Cache Bank 0 is selected first.

The initial content of two-way set associative cache is presented in Figure 4

## Valid         Tag                        Physical Page Number                   Dirty       Ref

| 1 | 0x0001A | 0x00467 | 1 | 0 |
| --- | --- | --- | --- | --- |
| 1 | 0x00002 | 0x004E2 | 0 | 1 |
| 0 | 0x00CF2 | 0x00188 | 0 | 0 |
| 1 | 0x00005 | 0x00782 | 1 | 0 |

| Page Table Register | 0x02C70000 |
| --- | --- |

#### Figure 2: Content of TLB and Page Table Register

## Memory Address      Valid      Dirty       Physical page number

| 0x02C70000 | 1 | 0 | 0x0041D |
| --- | --- | --- | --- |
| 0x02C70001 | 1 | 1 | 0x001D0 |
| 0x02C70002 | 1 | 0 | 0x004E2 |
| 0x02C70003 | 1 | 0 | 0x001FB |
| 0x02C70004 | 1 | 0 | 0x004B3 |
| 0x02C70005 | 1 | 1 | 0x00143 |
| 0x02C70006 | 1 | 0 | 0x004AC |
| 0x02C70007 | 1 | 1 | 0x002BC |
| 0x02C70008 | 1 | 0 | 0x00342 |
| 0x02C70009 | 1 | 1 | 0x00762 |

#### Figure 3: Content of the Page Table

Cache Bank 0  (Set 0)                                              Cache Bank 1 (Set 1)

| V | D | R | TAG | word 0 | word 1 | Index | V | D | R | TAG | word 0 | word 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 000 |  |  |  |  |  |  |
| 1 | 0 | 1 | 001D0C4 | 0013F212 | 01209168 | 001 | 1 | 0 | 0 | 004E2C1 | 01190244 | 01101020 |
| 1 | 0 | 1 | 003F020 | 0A012410 | 0200C0FA | 010 | 0 | 0 | 0 | 00AB200 | 00000000 | A3020000 |
| 1 | 0 | 1 | 004A000 | 2B480921 | 00000000 | 011 | 1 | 1 | 0 | 003A210 | 01A12320 | F1002A30 |
|  |  |  |  |  |  | 100 |  |  |  |  |  |  |
|  |  |  |  |  |  | 101 |  |  |  |  |  |  |
|  |  |  |  |  |  | 110 |  |  |  |  |  |  |
|  |  |  |  |  |  | 111 |  |  |  |  |  |  |

### Figure 4:  Two-way set associative cache

Note 1:  Empty cache entries have: V=0, D=0, R=0 and data words = 0x0000.

Note 2:  Cache entries are indexed from the top to bottom (top entry Index = 000

[binary]; bottom entry Index = 111 [binary])

## Question 2.1

## CPU issues the request to read data from the virtual address VA = 0x00002C13 (Rd),

## Determine the following:

- Virtual page # = ______________    Page offset      = ______________   (2 marks)

- TLB hit or miss ______________                                                               (1 mark )

- Physical page #  ______________   Physical address = _____________  (2 marks)

- Cache hit or miss _____________                                                              (2 marks)

Show: Block offset = _______, Index = ________, TAG =_0x________________

- Data to CPU     ______________                                                               (1 mark)

- Initiate the write back procedure?            Yes  or   No  (circle)               (1 mark)

- Indicate values of V, D and R bits in TLB after the reference:                (2 marks)

V = ________;  D = ________; R = _________

- Indicate values of V, D and R bits in Cache after the reference:              (2 marks)

Cache bank # _______; V = ________;  D = ________; R = _________

## Question 2.2

## CPU issues the request to write data to the virtual address VA = 0x000052A7 (Wr)

## Determine the following:

- Virtual page # = ______________    Page offset      = ______________   (2 marks)

- TLB hit or miss ______________                                                               (1 mark)

- Physical page# ______________   Physical address =______________   (2 marks)

- Cache hit or miss _____________                                                              (2 marks)

Show: Block offset = _______, Index = ________, TAG =_0x____________

- If miss, which block should be replaced (from which Cache bank):          (2 marks)

Indicate: Cache bank # _________; Word 0 = _________ Word 1=___________

- Will the “Write back” procedure be initiated?   Yes  or   No  (circle)         (1 mark)

If “Yes”, indicate start address in Main memory where the block has to be written back:

Start address = 0x_________________                                                              (1 mark)

Indicate physical start address of the block to be loaded into the Cache from the Memory:

Start address = 0x ________________                                                               (1 mark)

- Indicate values of V, D and R bits in TLB after the reference:                    (2 marks)

V = ________;  D = ________; R = _________

- Indicate values of V, D and R bits in Cache after the reference:                  (2 marks)

Cache bank # _______; V = ________;  D = ________; R = _________

## Question 2.3

## CPU issues the request to read data from the Virtual address = 0x000074F5 (Rd),

## Determine the following:

- Virtual page # = ______________    Page offset      = ______________ (2 marks)

- TLB hit or miss ______________                                                             (1 mark)

If miss, calculate the physical address of the Page Table entry where the physical page # of the requested data should be found

Page table entry address = 0x ________________                                        (2 marks)

Show calculations:______________________________________________________

Physical page #  ______________                                                                (1 mark)

- Physical address = 0x__________                                                            (1 mark)

- Cache hit or miss _____________                                                            (1 mark)

- Point by “ (” the best TLB-entry (in Figure 2.1) to be modified            (1 mark)

- New TAG content in the selected TLB entry = ____________                (1 mark)

- Indicate values of V, D and R bits in TLB after the reference:              (2 marks)

V = ________;  D = ________; R = _________

- Indicate values of V, D and R bits in Cache after the reference:              (2 marks)

Cache bank # _______; V = ________;  D = ________; R = _________

- New TAG content of the cache entry = ___________                                 (1 mark)

Section 3: Interfacing processor and peripherals, Hard Disk Drive & Bus

Hard Disk Drive Maxtor ATA100 - Model: STM305004N1AAA-RK) has the following specification:

a) Number of platters (disks) in the HDD = 4, b) Number of cylinders = 2086340,

c) Number of Sectors = 63, d) Sector size = 512 Bytes, e) Disk rotation speed =7200 rpm;

f) Maximum (guaranteed) seek time = 9 ms (time to find the initial sector of the page)

Question 3.1

For this Hard Disk Drive calculate the maximum number of pages to be stored if page size is equal to 4 K Words (1 word = 32 bits).

1) Total volume of HDD = _____________ G Bytes                                          (2 marks)

Show calculations

._____________________________________________________________________

2)  Number of pages to be stored in HDD = _______________                         (2 marks)

Show calculations

._____________________________________________________________________

Question 3.2

HDD-controller allows parallel data reading (writing) from (to) all platters of selected cylinder simultaneously. Page sectors can be accessed only sequentially.

Calculate maximum page fault penalty (time to replace page when page fault occurs), assuming that “Write back” procedure is always initiated (worst case scenario), page requires the maximum data access time and there is no HDD-controller’s overhead:

1) Cylinder volume = _____________ Kbytes                                                 (1 mark)

Show calculations_____________________________________________________

2) Number of pages stored at one cylinder = __________                                (2 marks)

Show calculations_____________________________________________________

3) Time to read (write) a page (without seek time overhead) assuming that all pages at one cylinder could be accessed during one rotation of the disk assembly

Page Rd / Wr time = _________ mS                                                                    (2 marks)

Show calculations_____________________________________________________

4) Calculate Page fault penalty in worst case scenario (when maximum seek time is required as well as “write back” procedure)

Page fault penalty = ________________ ms                                                     (2 marks)

Show calculations:

Section 4: Video-output subsystem organization

Specification: i) The video-output subsystem has to provide graphic video-output to standard HDTV-set (720p - progressive) with resolution 1280 pixels x 720 lines (rows) with 60 frames per second refresh rate; ii) The color resolution =  16.8 million colors (16,777,216). R,G and B color components should be encoded in equal number of bits.

iii) The video-output subsystem should also provide video-text generation to the HDTV-set working in character mode. Number of possible characters to be displayed = 255, number of characters in video-text is 80 characters per row and 30 rows / screen. Each character is displayed by 16 x 24 pixel matrix in one of 256 possible colors;

iv) The video-output subsystem should be implemented in the FPGA coupled with Video-RAM and RGB-to-HDTV Converter (Toshiba TC90240XBG ASIC). The block diagram of the video-system is presented in Figure 5.

Figure 5: Block diagram of the video-output subsystem

Question 4.1   Synchronous -signal generator:

Calculate the frequencies of the following:

i)   Vertical synchronization signal     Fvs = ________Hz                                (1 mark)

- Horizontal synchronization signal F hs = _____________KHz                 (1 mark)

Show calculations_________________________________________________

- Video-clock generator if each pixel generation needs 2 clock cycles.

Video-clock rate = ____________ MHz                                                    (1 mark)

Show calculations__________________________________________________________________

Question 4.2 Video-Frame memory (Graphic mode):

1) Calculate the total volume of Video-RAM in Graphic mode, which should have two pages. One page is used for displaying the current video-frame and another page is needed to accumulate the next video-frame.

The total number of bits per pixel: R ___ bit + G ___bit + B ____ bit = ______ bit/ pixel

(1 mark)

Total number of pixels / video-frame = _____________________ = pixels       (1 mark)

Thus, the total volume of the Video-RAM = _________MB                               (2 marks)

Show calculations_______________________________________________________

- Calculate required data access (cycle) time for Video-RAM memory chips:

Note: This time must not exceed pixel display time (assuming that R,G and B words can be accessed in parallel)

SRAM chip data access time = ________ ns                                                  (1 mark)

Show calculations_______________________________________________________

Question 4.3 Video-RAM (Character mode):

- Calculate the volume of the Character RAM (part of Video-RAM) which contains images of all 255 possible symbols (characters), when each symbol is encoded by 16 x 24 pixel matrix.

Total Character RAM volume = ___________ KB                                        (2 marks)

Show calculations____________________________________________________________

2) Calculate the volume of the Video-RAM to be reserved for encoding the video-text (80 characters per line x 30 lines), when symbol can be displayed in one of 256 colors.

Each symbol is encoded by ___________ bits                                              (1 mark)

Show calculations____________________________________________________________

Total Video-text memory volume = _________Bytes                                    (1 mark)

Show calculations__________________________________________________

Section 5: Bus arbitration and Direct Memory Access

The above embedded system is equipped with the I/O Processor to provide access to Main memory for the Video-output sub-system, HDD and I/O Ports (Figure 6)

Figure 6: Block diagram of I/O sub-system

Question 5.1

Circle the type of arbitration scheme used in the I/O Processor arbiter according to the Block diagram shown in Figure 6:                                                                     (1 mark)

- Centralized serial (Daisy chain) arbitration;

- Centralized parallel arbitration;

- Distributed arbitration with self-selection;

- Distributed arbitration by collision detection.

Question 5.2

According to Block diagram shown in Figure 6 determine the priority level for each I/O controller (Note: Highest priority is “1” and the lowest priority is “3”):            (1 mark)

a) Video-output controller priority level = ________

b) SCSI subsystem priority level =             ________

c) I/O Port controller priority level =          ________

Question 5.3

The SCSI-3 layer with Fast-80 feature (10 MHz, 16 bit parallel bus) is used to interface the above HDD with the virtual memory controller (see Figure 1) via I/O processor.

Calculate maximum SCSI-3 bus bandwidth = ____________MB/s                (2 marks)

Show calculations_________________________________________________

Question 5.4

The page replacement between Main memory and HDD is conducted in DMA Burst mode (Block transfer mode). The block size for page replacement procedure is equal to 16 words (1 word = 32 bits). The page size (according to Virtual Memory organization) is equal to 4K Words. Taking to the account SCSI-bus bandwidth determine the following:

- Period of time after granting the access to the Main memory for SCSI-controller (via I/O Processor) when CPU will not be able to communicate with the Main memory.

Note: Period of one block transfer from/to SCSI-controller does not have any HDD overhead because the requested page is already stored in SCSI FIFO-buffer.

Period of block transfer = __________ microsec.                                           (1 marks)

Show calculations______________________________________

- How many cycles of BR (Bus Request) & BG (Bus Grant) is needed for one complete page replacement (in worst case scenario when D-bit = 1 in any page fault case).

Number of Request / Grant cycles = _________                                        (2 marks)

Show calculations______________________________________

# Text boxes

CPU

FPGA:

Page Table Reg. +TLB

Two-Way Cache + SDRAM Controller +

VM Controller (Page exchange with HDD)

VM Address

CPU Data bus

Control signals

Video-Clock Generator

I/O subsystem interface

Clock Generator

I/O subsystem

interface

SDRAM:

Main memory

for program

and data pages

+ Page tables

Memory data bus

Control and synchronization signals

SDRAM Address

Ports

HDMI

Video-address

Control signals

Video-data bus

Video-RAM:

Video-Frame memory:

2 pages &

Character RAM

Vsync Hsync

RGB

Video-clock

FPGA:

Video-processor & Video-memory controller

RGB to

HDTV converter

TC90240XBG

BR

BG

BG

BR

I/O Port Controller

HDTV

Grant

Request

SCSI Controller

Hard Disk Drive

Video-Out Controller

BG

BR

I/O Processor,

Arbiter & Bridge